## Slide 1: Introduction to Microscopes

## Slide 2: Compound Light Microscopes
What are they?

## Slide 3
Instrument that allows you to view small objects. This type of microscope has more than one lens with its own light source that helps magnify objects unseen by the unaided eye.

## Slide 4
Label the Parts of the Microscope

## Slide 5
7 - Eyepiece
What you look through - usually has 10x magnification

## Slide 6
1 - Body Tube
Holds eyepiece in place

## Slide 7
8 - Arm
Support the body tube; used to carry microscope

## Slide 8
12 - Base
Supports the microscope; used to carry the microscope

## Slide 9
3 - Objective Lenses
Primary magnification source (ranges from 4x - 40x magnification)
LOW: 4x
MEDIUM: 10x
HIGH: 40x

## Slide 10
2 - Turret
Holds objective lenses & turns them into place

## Slide 11
9 - Stage
Where slide is placed; can be moved up/down using adjustment knobs

## Slide 12
4 - Stage Clips
Holds the microscope slide in place

## Slide 13
10 - Coarse Adjustment Knob
Focus the microscope
Only to be used with LOW and MEDIUM power objective lenses

## Slide 14
11 - Fine Adjustment Knob
Focus the microscope
Used with HIGH- power objective lens

## Slide 15
6 - Light
Illuminates the slide

## Slide 16
5 - Diaphragm
Controls amount of light

## Slide 17: Rules
what to follow when using microscopes

## Slide 18: Videos for Microscope Handling
Basic How to Use
https://www.youtube.com/watch?v=zzamomqlwxU&ab_channel=Dr.JoycePatrick
Troubleshooting
https://www.youtube.com/watch?v=SUo2fHZaZCU&ab_channel=FresnoState

## Slide 19: How to Handle Microscopes
Use 2 hands to carry the microscope - one at the arm & the other supporting the base
Care for the electrical cord - beware of tripping hazards
Do not touch the lens with your fingers - use proper lens tissue to clean the surfaces

## Slide 20: How to Handle Microscopes
Do not adjust any knobs until you are ready to use the microscope
Always focus using the coarse adjustment knob first - with the low-power objective lens. Then focus on medium-power.
Only use the fine adjustment knob with the high-power objective lens
Always be gentle when handling microscopes & slides

## Slide 21: Wet Mounts
how to prepare a slide

## Slide 22: Preparing Slides
Clean the slide & cover slip
Place the object in the centre of the slide - add 2 drops of water & carefully lower cover slip on top
  Lower the cover slip at an angle to prevent bubbles
Remove excess water with paper towel - touch to side of cover slip

## Slide 23
Preparing a Wet Mount

## Slide 24: Magnification
how much is the image amplified?

## Slide 25: Total Magnification = Eyepiece Magnification x Objective Lens Magnification
OBJECTIVE LENS | MAGNIFICATION | TOTAL MAGNIFICATION
Low-Power | 4 x | 10 x 4 = 40 x
Medium-Power | 10 x | 10 x 10 = 100 x
High-Power | 40 x | 10 x 40 = 400 x

## Slide 26: Biological Drawings
sketching out what you see

## Slide 27: Important Features of Sketches
Use a pencil
Use stippling (point-like pencil marks) to show darker areas
Title
Labels on the right with extending lines
Magnification used to view
Source: NC STATE UNI

## Slide 28
Source: BIOLOGY 4 A LEVEL

## Slide 29: Clean Up
how to properly store microscopes

## Slide 30: Follow the acronym:
C - cord wrapped
L - light off
O - objective lens to LOW
S - stage lowered
E - eyepiece rotated
Cover up the microscope when not in use.

## Slide 31: How To Demo
viewing a slide

## Slide 32: How to Use a Microscope!
Set up microscopes - follow the rules!
LOW-power objective lens locked into place
Look through eyepiece - adjust diaphragm until view is the brightest it can be
Secure the slide in place using the stage clips - object is in centre of the stage opening
Look through eyepiece - adjust coarse knob slowly until object in focus
  Use fine adjustment knob to sharpen focus

## Slide 33: How to Use a Microscope!
Once in focus at LOW power, rotate nosepiece to MEDIUM-power lens
  Be sure that the objective lens does not hit the surface of the slide (look from the side)
View object under HIGH-power lens (follow same procedure as above)
Draw a sketch of what you see- use tips provided!
Rotate nosepiece to LOW, return slide to proper container - follow clean up procedure

## Slide 34: THANKS!
Any questions?

## Slide 35: How to Use a Microscope!
Set up microscopes - follow the rules!
LOW-power objective lens locked into place
Look through eyepiece - adjust diaphragm until view is the brightest it can be
Secure the slide in place using the stage clips - object is in centre of the stage opening
Look through eyepiece - adjust coarse knob slowly until object in focus
  Use fine adjustment knob to sharpen focus

## Slide 36: How to Use a Microscope!
Once in focus at LOW power, rotate nosepiece to MEDIUM-power lens
  Be sure that the objective lens does not hit the surface of the slide (look from the side)
View object under HIGH-power lens (follow same procedure as above)
Draw a sketch of what you see- use tips provided!
Rotate nosepiece to LOW, return slide to proper container - follow clean up procedure

## Slide 37: Total Magnification = Eyepiece Magnification x Objective Lens Magnification
OBJECTIVE LENS | MAGNIFICATION | TOTAL MAGNIFICATION
Low-Power | 4 x | 10 x 4 = 40 x
Medium-Power | 10 x | 10 x 10 = 100 x
High-Power | 40 x | 10 x 40 = 400 x

## Slide 38: Follow the acronym:
C - cord wrapped
L - light off
O - objective lens to LOW
S - stage lowered
E - eyepiece rotated
Cover up the microscope when not in use.

## Slide 39: Biological Drawings
sketching out what you see

## Slide 40: Important Features of Sketches
Use a pencil
Use stippling (point-like pencil marks) to show darker areas
Title
Labels on the right with extending lines
Magnification used to view
Source: NC STATE UNI

## Slide 41
Source: BIOLOGY 4 A LEVEL

## Slide 42: Microscope Lab/Investigation

## Slide 43
PROBLEM | HOW TO SOLVE
You see nothing...it looks black. | Microscope plugged in, light is on.
You can’t find anything on the slide. | Solution 1: Check with your naked eye that the object is in the middle of stage opening. If not, adjust its position. Solution 2: Using the low power lens, lower stage all the way & raise it slowly with the coarse adjustment knob.
Image is very faint or too bright. | Adjust diaphragm.
You see lines & specks floating across the slide. | Structures in the fluid of your eyeball - this is normal!
You see a double image. | Objective lens clicked into place.
Your eyes feel tired & you can’t sketch the object. | Keep both eyes open.
You can’t see the object when you go from low to medium/high power | Start from the beginning at low power. Centre the slide in the field of view before changing to higher magnification lens.

## Slide 44
Extra resources

## Slide 45
SlidesCarnival icons are editable shapes.
This means that you can:
Resize them without losing quality.
Change fill color and opacity.
Isn’t that nice? :)
Examples: